## Slide 1: NDN in Local Area Networks
Junxiao Shi
The University of Arizona
2014-09-04

## Slide 2: Why are we interested in LAN?
We use local area network everyday. It's an important scenario for NDN project.
NDN deployment on local area network is much easier: customer has full control, and doesn't need to coordinate with ISP.
Types of local area networks
home
networks
office
networks
data center
networks

## Slide 3: Office Networks
Office network: the "typical" local area network
Characteristics
  dozens to hundreds of desktop and laptop computers
  wired and wireless connections
  There is a network administrator

## Slide 4: Finding Contents
Problem: Consumer asks for a content by its Name. How to find the content?
Solution 1: Producer announces the prefix it serves.
  Choice 1: all nodes remember and exchange prefixes
  Chocie 2: directory server(s) remembers prefixes
Solution 2: Consumer floods a request to locate the contents.
  Choice 1: flood the actual Interest
  Choice 2: flood a query Interest to locate the producer

## Slide 5: Finding Contents
producer announces prefix
Benefit: no flooding when retrieving contents
Drawback: a separate control protocol is needed
Drawback: many in-network states to remember producer for each content prefix
consumer floods request
Benefit: everything is in the data layer
Benefit: no in-network state until contents are retrieved
Drawback: many floodings during data retrieval
Both can work fine in office networks, but which one to choose depends on network size, how many contents are there and how often they are requested, how often nodes join/leave the network.

## Slide 6: Traffic Separation and Policy
Today's office networks often configure VLANs.
  VLAN gives network administrator an opportunity to enforce network policy, because communication across Ethernet VLANs must go through layer-3 router,.
NDN operates on layer-3, and Data can be encrypted.
Problem: How do we enforce network policy?

## Slide 7: Traffic Separation and Policy
Enforce policy through VLAN-like traffic separation
Benefit: "physical" separation, policy enforcement does not rely on trust model
Drawback: switches are more complex
How to support traffic separation in NDN?
Enforce policy through encryption
Benefit: switches are simpler and faster
Drawback: everything (including Name) not completely public must be encrypted
How to design a trust model for policy?

## Slide 8: Home Networks
Characteristics:
  a variety of devices, more than just computers
    laptop/tablet/phone/TV
    smart home gadgets: lights, power outlets, scales, security cameras, etc
  wireless connection
  no network administrator: configuration must be mostly automated and require minimal user effort

## Slide 9: Finding Contents in Home
producer announces prefix
Home router serves as directory server.
Benefit: does not drain battery
Drawback: memory usage on home router – less memory for caching
Challenge: producer mobility support in larger homes with multiple access points
consumer floods request
Benefit: no in-network state until contents is retrieved
Benefit: supports producer mobility well
Drawback: battery-powered gadgets must process flooded requests even if they don't have contents

## Slide 10: Unified Protocol for Gadgets
Today's smart home gadgets use proprietary protocols. They cannot interoperate.
In NDN, we can define unified protocol based on Interest-Data exchange, so that they can interoperate, and can be controlled by a single mobile app.

## Slide 11: Data Center Networks
Characteristics: many servers connected via carefully planned wired network, many contents are served and transmitted
Finding contents: scalability is biggest challenge
Policy: needed in multi-tenant data center
Performance and reliability are important

## Slide 12: Works in Progress
at The University of Arizona

## Slide 13: Self-learning Forwarding Strategy
Self-learning is a solution for finding contents in office network. The basic idea is to let consumer flood the first Interest, and learn the path toward producer for use with subsequent Interests.
On every node, FIB starts with only local producers. All paths are learnt dynamically.

## Slide 14: Self-learning Idea
face 1
face 2
face 3
Interest
/A/0
learnt paths
Interest
/A/0
Data
/A/0
/A face 2
Interest
/A/1
Data
/A/1

## Slide 15: Self-learning Highlights
Strategy can find best path.
  16-host fat tree topology: average path stretch is 1.018, 96.01% packets take shortest path.
Path availability and quality are monitored.
  If link failure or performance degradation is detected, strategy will try another path or flood again.
  No packet loss is observed in link failure experiments.
Strategy is adaptive.
  Periodical probing finds new or recovered paths.
  Strategy switches to a better path if available.

## Slide 16: NDN on Home Router
NFD has been cross-compiled for home routers with OpenWrt and DD-WRT platforms.
Even with the limited resources available (CPU, memory, storage), NDN performs well.
NDN home routers are useful for
  home network experiments
  small testbed: sixteen hosts and five home routers

## Slide 17: Hadoop on NDN
Hadoop: framework for large-scale data processing, commonly used in data centers
We are working on getting Apache Hadoop to run on NDN.
Short-term goal: make minimal changes to Hadoop
  directly map RPC calls to NDN Interest-Data exchanges
Long-term goal: make Hadoop and applications native to NDN
  We hope unique properties of NDN, such as in-network caching, will make Hadoop faster and more efficient.